## Slide 1: FAILURE MODE EFFECT ANALYSIS
Prof. R. Saravanan
Annamalai University

## Slide 2: FMEA
A failure mode and effect analysis (FMEA) is a type of hazard review that probes the failures of components within a process or system and the resultant effects of those failures
FMEA methodology is largely equipment oriented
This technique is useful in analyzing single failure modes that result in unwanted situations and not efficient for reviewing large number of multiple component failures

## Slide 3: FMEA
Step 1: Formation of review team
Step 2: Gathering documents
Step 3: Conducting FMEA
  Identify and describe the equipment
  Determine the failure modes
  Determine the effects of failures
  Judge the risk
  Recommendations for Action
Step 4: Reporting the Results

## Slide 4: Conducting FMEA
  Identify and describe the equipment
  All the major equipment are listed in the order in which they appear on the P & I Diagram
  Each piece of equipment has to be “checked off” for its failure modes
  Ensure that the equipment is identified in ways (V-141) that the reviewers can understand and usable later by others who act upon recommendations

## Slide 5: Conducting FMEA…
Determine the failure modes
    For each component or piece of equipment listed, determine all of the possible failure modes that are consistent with the equipment operation
Determine the Effects of the Failures
  The review team shall carefully examine and consider all the immediate effects of those determined failure modes
Judge the Risk
  The review team then makes a judgment about the risks around each of the equipment failures and associated effects and classify its severity/consequences.

## Slide 6: Conducting FMEA…
Recommendations for Action
  Based on the identification of failure modes determined for each of the situations, the team then shall make recommendations.
  Discussions and brain storming sessions at each failure modes are carried and suitable preventive techniques/suggestions will be recommended.

## Slide 7: Reporting the Results
  The information developed during the analysis needs to be communicated for important findings and it shall be directed towards its implementation to overcome the failures.
  A tabular nature of worksheet is prepared by the team and submitted for all of the findings

## Slide 8: FMEA Work Sheet

## Slide 11: FMEA – Pros and Cons
Well suited for equipment oriented systems
Limited to single failure modes
For complex mechanical or electrical systems that has multiple operator interface opportunities, FMEA is out of scope

## Slide 12
THANK YOU