## Slide 1: FAULT TREE ANALYSIS
Prof. R. Saravanan
Annamalai University

## Slide 2: F T A
A fault tree is a graphical representation of the logical relations between an UNDESIRED EVENT known as TOP EVENT, and the PRIMARY CAUSE EVENTS

## Slide 3: F T A
A Fault Tree is constructed by defining a TOP EVENT and then defining cause events with the LOGICAL relations between them

## Slide 4: Elements of F T A
The main elements of the FTA are
Event Definitions and
Logic Gates

## Slide 5: Event Definitions
Primary Failure
Fault Event

## Slide 6: Logic Gates
AND
OR

## Slide 7: Steps of F T A
Step 1: TOP EVENT (undesired event)
Step 2: Fault Tree Construction
Step 3: Analysis of Fault Tree
Step 4: Reporting Minimal Cut sets

## Slide 8: Step 1: TOP EVENT (undesired event)
The Top Event must be sufficiently defined so that the evaluation can be conducted efficiently and results will be credible
Helps to focus quickly

## Slide 9: Step 2: Fault Tree Construction
Starting with the top unwanted event, the analyst then constructs in a logical, sequential fashion all the contributing fault events until the primary events are arrived

## Slide 10: Example
MOTOR OVERHEATS
Primary Motor Failure
Excessive Current to Motor
Excessive Current in Circuit
Fuse fails to Open
Primary Wiring Failure
Primary Power Supply Failure
Primary Fuse Failure
OR
(C)
AND
OR
(B)
(A)
(1)
(2)
(3)
(4)

## Slide 11: Step 3: Analysis of Fault Tree
Construction of Matrix
GATE | TYPE OF GATE | No. of Inputs | Input Code No.
A | OR | 2 | 1 B
B | AND | 2 | C 2
C | OR | 2 | 4 3

## Slide 12: Step 3: Analysis of Fault Tree Construction of Matrix…
If the Gate is an OR gate, replace by input code Vertically
If the Gate is an AND gate, replace by input code Horizontally
Minimal Cut Sets: (1), (4, 2) and (3, 2)
A (OR) | 
1 | 
B (AND) | 
1 | 
C (OR) | 
1 | 
4 | 2
3 | 2

## Slide 13: Step 4: Reporting Minimal Cut sets
Causes for the Top Event from the Cut sets
  (1) Primary Motor Failure
  (4, 2) Primary power supply failure and Primary fuse failure
  (3, 2) Primary wiring failure and Primary fuse failure

## Slide 14: Thank You…
Respect Parents