## Slide 1
Fire & Explosion Index
Dr. R. Saravanan M.E., DIS, Ph.D
Professor
Department of Chemical Engineering
Annamalai University

## Slide 2: Overview
Introduction
Calculation procedure
Significance

## Slide 3
Introduction
The Dow Fire & Explosion Index (FEI) provides a simple method to help determine the areas of greatest loss potential in a particular process.
It also enables one to predict the physical damage that would occur in the event of an incident.
Absolute measures of risk are very difficult to determine, but the FEI system will provide a method of ranking one hazard relative to another.

## Slide 4: Where this FEI is used?
For conducting an initial Process Hazard Analysis (PHA).
As a screening tool for further study
In Emergency Response Planning (ERP)

## Slide 5: DOW F & EI
The Dow F&EI is a ranking system that gives a relative index to the risk of individual process units due to potential fires and explosions.
It has been revised six times since 1967. The latest: 7th edition
It ranks individual process units where special safety attention ought to be focused.

## Slide 6: DOW F & EI
It is valuable as a guide to decide whether it is necessary to consider less hazardous materials and/or other process routes.
It helps engineers to be aware of the hazards in each process unit while making important decisions in reducing the severity and/or the probability of the potential incident.

## Slide 7: When should one perform an F&EI analysis?
P&IDs have been completed.
It is performed after all equipment are sized and details of the process are determined.
A trial equipment layout has been done.

## Slide 8: Generally a senior process engineer, who is acquainted with the details of the project, is assigned the task.
Who Usually Performs the FEI?

## Slide 9: Before F & EI Calculation
Chemical energy potential (material factor)
Quantity of hazardous material
Operating pressure and temperature

## Slide 10: What does the F & EI Consists of?
6 General Process Hazards (F1)
12 Special Process Hazards (F2)
Material Factor (MF) is obtained from reactivity value (NR) and flammability value (NF).

## Slide 11: F & EI Range

## Slide 12: 6 General Process Hazards
1. Exothermic reactions
Mild exothermic reaction (hydrogenation, hydrolysis, isomerization etc.) 0.30
Moderate exothermic reaction (alkylation, addition rxns, polymerization etc.) 0.50
Critical to control exothermic reactions (halogenation) 1.00
Particularly sensitive exothermic (nitration) 1.25

## Slide 13: 6 General Process Hazards
2. Endothermic Processes
All endothermic processes in the reactor 0.20
Energy for the endothermic processes is provided by combustion of a solid, liquid or gaseous fuel 0.40

## Slide 14: 6 General Process Hazards
3. Material handling and transfer
The (un)loading process of Class I flammables or LPG chemicals 0.50
The air present in the centrifuges, batch reactors, or mixers 0.50
Warehouse storages or yard storages (not storage tanks) involving chemical with potential fire hazards 0.85, 0.65, 0.40, or 0.25 (depends on flammability of the chemicals handled.)
Utilizing racks without in-rack sprinkler 0.20

## Slide 15: 6 General Process Hazards
4. Enclosed or indoor process units
Dust collectors 0.50
Handling flammable fluids at a T > F.P 0.30(> 1,000 gallons 0.45)
Liquefied petroleum gas (LPG) or any flammable fluids handled at T > B.P. 0.60 (>10,000 lb 0.90)
All of the penalties above will be reduced by 50% if mechanical ventilation is properly designed for the fire hazard

## Slide 16: 6 General Process Hazards
5. Access
warehouse >25,000 ft2 0.35
6. Drainage and spill control
Diking which prevents the spill from reaching other areas but expose all the equipment within the dike or flat areas around process 0.50
If a basin or trench exposes utility lines or does not meet the required distance 0.50

## Slide 17: 12 Special Process Hazards (F2)
Toxic materials.
Sub-atmospheric pressure (<500 mmHg).
Operating in or near flammable range
Dust explosion.
Pressure
Low temperature.
Quantity of flammable/unstable material
Corrosion and Erosion
Leakage – joints and packing.
Use of fired equipment.
Hot oil heat exchanger system.
Rotating equipment.

## Slide 18: Material Factor

## Slide 19: Calculating Radius and Area of Exposure
Radius of Exposure
Area of Exposure

## Slide 20
Any Questions?
Please……

## Slide 21
Thank You